## Slide 1: Quality Control (Ch.10)
  CYCU
  Prof. CK Farn
mailto: ckfarn@gmail.com
http://www.mgt.ncu.edu.tw/~ckfarn/cycu
  2022.11
8

## Slide 2: What Is Quality Control?
A process that evaluates output relative to a standard and takes corrective action when output doesn’t meet standards
  If results are acceptable no further action is required
  Unacceptable results call for correction action
Inspection alone is not sufficient to achieve a reasonable level of quality
  Most organizations rely upon some inspection and a great deal of process control to achieve an acceptable level of quality

## Slide 3: Phases of Quality Assurance

## Slide 4: Inspection
An appraisal activity that compares goods or services to a standard
Inspection issues:
  How much to inspect and how often
  At what points in the process to inspect
  Whether to inspect in a centralized or on-site location
  Whether to inspect attributes or variables

## Slide 5: How Much to Inspect

## Slide 6: Where to Inspect in the Process
Typical inspection points:
  Raw materials and purchased parts
  Finished products
  Before a costly operation
  Before an irreversible process
  Before a covering process

## Slide 7: Example of inspection at a Hotel/Motel
Inspection Point | Characteristics
Accounting/billing | Accuracy, timeliness
Building and grounds | Appearance and safety
Main desk | Appearance, waiting times, accuracy of bills
Maid service | Completeness, productivity
Personnel | Appearance, manners, productivity
Reservations/occupancy | Over/underbooking, percent occupancy
Restaurants | Kitchen, menus, meals, bills
Room service | Waiting time, quality of food
Supplies | Ordering, receiving, inventories

## Slide 8: Off-Site vs. On-Site Inspection
Effects on cost and level of disruption are a major issue in selecting centralized versus on-site inspection
Off-Site
  Specialized tests that may best be completed in a lab
    More specialized testing equipment
    More favorable testing environment
On-Site
  Quicker decisions are rendered
  Avoid introduction of extraneous factors
  Quality at the source

## Slide 9: Statistical Process Control (SPC)
Quality control seeks quality of conformance
  A product or service conforms to specifications
A tool used to help in this process:
  SPC
    Statistical evaluation of the output of a process
    Helps us to decide if a process is “in control” or if corrective action is needed

## Slide 10: Process Variability
Two basic questions concerning variability:
  Issue of process control
    Are the variations random? If nonrandom variation is present, the process is said to be unstable.
  Issue of process capability
    Given a stable process, is the inherent variability of the process within a range that conforms to performance criteria?

## Slide 11: Variation
Random (common cause) variation:
  Natural variation in the output of a process, created by countless minor factors
Assignable (special cause) variation:
  A variation whose cause can be identified
  A nonrandom variation

## Slide 12: Sampling and Sampling Distribution
SPC involves periodically taking samples of process output and computing sample statistics:
  Sample means
  The number of occurrences of some outcome
Sample statistics are used to judge the randomness of process variation

## Slide 13: Sampling and Sampling Distribution (cont.)
FIGURE 10.4A The sampling distribution of means is normal, and it has less variability than the process distribution, which might not be normal

## Slide 14: Control Process
Sampling and corrective action are only a part of the control process
Steps required for effective control:
  Define: What is to be controlled?
  Measure: How will measurement be accomplished?
  Compare: There must be a standard of comparison
  Evaluate: Establish a definition of out of control
  Correct: Uncover the cause of nonrandom variability and fix it
  Monitor: Verify that the problem has been eliminated

## Slide 15: Control Charts: The Voice of the Process
A time-ordered plot of representative sample statistics obtained from an ongoing process (for example, sample means), used to distinguish between random and nonrandom variability
Control limits
  The dividing lines between random and nonrandom deviations from the mean of the distribution
  Upper and lower control limits define the range of acceptable variation

## Slide 16: Control Chart
Each point on the control chart represents a sample of n observations

## Slide 17: Errors
Type I error
  Concluding a process is not in control when it actually is.
    The probability of rejecting the null hypothesis when the null hypothesis is true
    Manufacturer’s risk
Type II error
  Concluding a process is in control when it is not.
    The probability of failing to reject the null hypothesis when the null hypothesis is false
    Consumer’s risk

## Slide 18: Type I Error

## Slide 19: Observations from Sample Distribution

## Slide 20: Control Charts for Variables
Variables generate data that are measured
  Mean control charts
    Used to monitor the central tendency of a process
      “x-bar” charts
  Range control charts
    Used to monitor the process dispersion
      R charts

## Slide 21: Establishing Control Limits

## Slide 22: X-Bar Chart: Control Limits
Used to monitor the central tendency of a process

## Slide 23: Range Chart: Control Limits
Used to monitor process dispersion

## Slide 24
Factors for Three Sigma Control Charts
 |  |  | FACTORS FOR R CHARTS
Number of Observations in Sample, n | Factor for Chart, A2 | Lower Control Limit, D3 | Upper Control Limit, D4
2 | 1.88 | 0 | 3.27
3 | 1.02 | 0 | 2.57
4 | 0.73 | 0 | 2.28
5 | 0.58 | 0 | 2.11
6 | 0.48 | 0 | 2.00
7 | 0.42 | 0.08 | 1.92
8 | 0.37 | 0.14 | 1.86
9 | 0.34 | 0.18 | 1.82
10 | 0.31 | 0.22 | 1.78
11 | 0.29 | 0.26 | 1.74
12 | 0.27 | 0.28 | 1.72
13 | 0.25 | 0.31 | 1.69
14 | 0.24 | 0.33 | 1.67
15 | 0.22 | 0.35 | 1.65
16 | 0.21 | 0.36 | 1.64
17 | 0.20 | 0.38 | 1.62
18 | 0.19 | 0.39 | 1.61
19 | 0.19 | 0.40 | 1.60
20 | 0.18 | 0.41 | 1.59
TABLE 10.3
Factors for three-sigma control limits for X and R charts
Source: Adapted from Eugene Grant and Richard Leavenworth, Statistical Quality Control, 5th ed. Copyright ©1980 McGraw-Hill Companies, Inc. Used with permission

## Slide 25: Mean and Range Charts A

## Slide 26: Mean and Range Charts B

## Slide 27: Using Mean and Range Charts
To determine initial control limits:
  Obtain 20 to 25 samples
  Compute appropriate sample statistics
  Establish preliminary control limits
  Determine if any points fall outside of the control limits
    If you find no out-of-control signals, assume the process is in control
    If you find an out-of-control signal, search for and correct the assignable cause of variation
  Resume the process and collect another set of observations on which to base control limits
  Plot the data on the control chart and check for out-of-control signals

## Slide 28: Control Charts for Attributes
Attributes generate data that are counted.
  p-chart
    Control chart used to monitor the proportion of defectives in a process
  c-chart
    Control chart used to monitor the number of defects per unit

## Slide 29: Use a p-chart:
When observations can be placed into two categories
  Good or bad
  Pass or fail
  Operate or don’t operate
When the data consists of multiple samples of several observations each

## Slide 30: p-chart Control Limits

## Slide 31: Use a c-chart:
Use only when the number of occurrences per unit of measure can be counted; non-occurrences cannot be counted.
  Scratches, chips, dents, or errors per item
  Cracks or faults per unit of distance
  Breaks or tears per unit of area
  Bacteria or pollutants per unit of volume
  Calls, complaints, failures per unit of time

## Slide 32: Managerial Considerations
At what points in the process to use control charts
What size samples to take
Sample frequency
What type of control chart to use
  Variables
  Attributes

## Slide 33: Run Tests
Even if a process appears to be in control, the data may still not reflect a random process
Analysts often supplement control charts with a run test
  Run test
    A test for patterns in a sequence
  Run
    Sequence of observations with a certain characteristic

## Slide 34: Nonrandom Patterns

## Slide 35: Process Capability
Once a process has been determined to be stable, it is necessary to determine if the process is capable of producing output that is within an acceptable range
Tolerances or specifications
  Range of acceptable values established by engineering design or customer requirements
Process variability
  Natural or inherent variability in a process
Process capability
  The inherent variability of process output (process width) relative to the variation allowed by the design specification (specification width)

## Slide 36: Process Capability (cont.)

## Slide 37: Cp

## Slide 38: Cpk
Used when a process is not centered at its target, or nominal, value

## Slide 39: Improving Process Capability
Simplify
Standardize
Mistake-proof
Upgrade equipment
Automate

## Slide 40: Taguchi Loss Function

## Slide 41: Limitations of Capability Measures
There are several risks of using capability measures:
  The process may not be stable
  The process output may not be normally distributed
  The process is not centered but Cp is used

## Slide 42: Assignment (team)
The Toyota Production System (TPS) has been studied in the POM field since the late 1970s. There are various aspects to TPS. Conduct a study on the application of the TQM concept in Toyota.
Prepare a ppt presentation no more than 8 pages on this Topic.
Due Dec. 15